## Slide 1: SENSORSHLD1-EVK-101 Usage Guide
October 26, 2016
Kris Bahar
Applications Engineer

## Slide 2: Good References
ROHM General Page:
  http://www.rohm.com/web/global/multi-sensor-shield
Design Files and FW Examples
  https://github.com/ROHMUSDC/ROHM_SensorPlatform_Multi-Sensor-Shield

## Slide 3: General Info: SENSORSHLD1-EVK-101
Power ON LED
Temperature Sensor
Pressure Sensor
Accel + Mag Sensor
UV Sensor
Magnetometer Sensor
Accelerometer
Accelerometer
Accelerometer
Hall Switch Sensor
Gyro Sensor
Color Sensor
ALS/Prox Sensor
Accelerometer

## Slide 4: General Info: Board Power
VDD
GND
Power is routed to the board via H4 Header
NOTE: Be sure that this is connected to 3.3V only; some sensors on board will break due to 5V

## Slide 5: Setup: Arduino Recommended Rework
On the Arduino UNO board, the I2C pins connected to the top left header are routed to pins A4 and A5 on the bottom right connector.
This conflicts with the UV sensor’s ADC output.
Thus, to reroute this on our board, we suggest the following rework…
  Disconnect existing nets by removing R27, R31
  Reconnect UV sensor ADC by connecting the top pad of R31 to the bottom pad of R27
Arduino Uno R3 Schematic
ROHM Shield Rework Recommendation

## Slide 6: Setup: Environment Preparation
Needed: Install the Arduino Software IDE.
  https://www.arduino.cc/en/Guide/Windows
Recommended: Install TeraTerm
  Recommendation since serial monitor is available within the Arduino IDE.
  However, this includes good functions such as logging display of special ASCI character sets.
  https://ttssh2.osdn.jp/index.html.en

## Slide 7: Setup: Download Code and Open in Arduino IDE
Download the example sensor shield code found in the GitHub Repository
  https://github.com/ROHMUSDC/ROHM_SensorPlatform_Multi-Sensor-Shield
    …/Platform Code/Arduino_UNO_FirmwareExample/
Open the file named “ROHM_SENSORSHLD1-EVK-101_10-20-2016.ino” in the Arduino IDE
Install the SoftI2CMaster Library.
  We can not use the general “wire” library for standard I2C because we want to utilize the repeated start bit of the I2C interface protocol to properly read data back from our sensor devices
  Instructions on how to install
    http://playground.arduino.cc/Main/SoftwareI2CLibrary
  Where to download the library itself
    https://github.com/felias-fogg/SoftI2CMaster

## Slide 8: Setup: Flash Board and View Output
In order to flash the board, click the “verify” button to compile your code.
Once this completes and returns with no errors, click the “upload” button
The dialog box will return with “Done uploading” when complete
To view the sensor output, open the serial monitor or Tera Term
If using Tera Term, configure the Tera Term Serial Port to the above settings (Setup -> Serial Port)
Then, open a new connection (Alt-N), select the appropriate COM port, and click OK
Once completed, the connection will open and sensor data will stream to the console
Verify

## Slide 9: Sensor Explanation: BDE0600G Temp Sensor
Datasheet:
  http://rohmfs.rohm.com/en/products/databook/datasheet/ic/sensor/temperature/bdexxx0g-e.pdf
Communication Interface:
  Analog Output
  Thermostat Interrupt (55°C to 115°C in 5°C steps)
How to Convert:
  Known Values
    Temperature Sensitivity = -10.68mV/degC
    Temp Known Point = 1.753V @ 30 degC
  Calculation
    ADC_Voltage = (sensorValue / 670) * 3.3V
    ADC_Voltage = sensorValue * 0.004925
    Temperature (in deg C) = (ADC_Voltage - 1.753)/(-0.01068) + 30
Typical Use Cases:
  Temperature Detection
  Battery Management
  Heat Management
  Thermostat Interrupt Detection

## Slide 10: Sensor Explanation: ML8511 UV Sensor
Datasheet:
  http://media.digikey.com/pdf/Data%20Sheets/Rohm%20PDFs/ML8511_3-8-13.pdf
Communication Interface:
  Analog Output
What does this measure?
  UV intensity in mW/cm2
How to Convert:
  Known Values
    UV Sensitivity = 0.129 V/(mW/cm2)
    Temp Known Point = 2.2V @ 10mW/cm2
  Calculation
    ADC_Voltage = (sensorValue / 670) * 3.3V
    ADC_Voltage = sensorValue * 0.004925
    UV Intensity (in mW/cm2) = (ADC_Voltage - 2.2)/(0.129) + 10
Typical Use Cases:
  Outdoor Detection
  UV Index Approximation

## Slide 11: Sensor Explanation: BU52014 Hall Sensor
Datasheet:
  http://rohmfs.rohm.com/en/products/databook/datasheet/ic/sensor/hall/bu52004gul-e.pdf
Communication Interface:
  Digital Logic Output (H/L)
What does this measure?
  Magnetic Flux Presence
How to Interpret:
  OUT1/GPIO0 is tied to South Pole Detection Pin
    Pin Output LOW on South Detect
  OUT2/GPIO1 is tied to North Pole Detection Pin
    Pin Output LOW on North Detect
Typical Use Cases:
  Contactless Switch
  Tablet/Phone Case

## Slide 12: Sensor Explanation: KMX62 Accel + Mag Sensor
Datasheet:
  http://kionixfs.kionix.com/en/datasheet/KMX62-1031%20Specifications%20Rev%203.0.pdf
Communication Interface:
  I2C
What does this measure?
  Acceleration, 3 Axis, 14bit, ±16g
  Magnetic Flux, 3 Axis, 14bit, ±1200µT
How to Interpret
  Perform 12 Bytes I2C Data Read
  Format 12 Bytes of Data into the six 14bit raw sensor output (Accel X/Y/Z, Mag X/Y/Z)
  Convert Using Appropriate Scheme
    ACCEL = Axis_ValueInG = MEMS_Accel_axis / 2048
    MAG = Axis_ValueInuT = MEMS_Mag_axis / 0.146
Typical Use Cases:
  Low Power Gyro
  Compass Orientation

## Slide 13: Sensor Explanation: BM1383 Pressure Sensor
Datasheet:
  http://rohmfs.rohm.com/en/products/databook /datas heet/ic/sensor/pressure/bm1383glv-e.pdf
Communication Interface:
  I2C
What does this Measure?
  Barometric Pressure, 16bit + 5bit decimal, 300hPa to 1100hPa
How to Convert:
  Perform 3 Bytes I2C Data Read
  Format 3 Bytes of Data into the pressure output conversion formula
    Pressure Value[hPa] = { PRESS_OUT[15:8], PRESS_OUT[7:0], PRESS_OUT_XL[5:0] } / 2048
Typical Use Cases:
  Height/Altitude Detection

## Slide 14: Sensor Explanation: RPR-0521 ALS+PROX Sensor
Datasheet:
  http://www.rohm.com/web/global/datasheet/RPR-0521RS
Communication Interface:
  I2C
What does this measure?
  Ambient Light, 0 to 43000 Lx
  Proximity Detection, within 100mm maximum
How to Convert:
  Perform 6 Bytes I2C Data Read (4 for ALS, 2 for Prox)
  Format 4 Bytes of Data into 16bit values for DATA0 (Visible Light) and DATA1 (Infrared Light)
  Format 2 Bytes of Data into 16bit value for Proximity ADC Counts
  Perform Conversion of Raw Data to Lx (see next slide)
Typical Use Cases:
  Mobile Phones (brightness optimization and ear detect)
  Contactless Switch/Presence Detection

## Slide 15: ALS Sensor Conversion Equation
Q: Why does this equation look so complex?
A: This ALS sensor utilizes 2 photodiodes, one for visible light and one for ambient light.
This ratio based piecewise function allows us to properly reject high IR based output and generate a good lux output based on the actual visible light spectrum

## Slide 16: Sensor Explanation: BH1745NUC Color Sensor
Datasheet:
  http://rohmfs.rohm.com/en/products/databook/ datasheet/ic/sensor/light/bh1745nuc-e.pdf
Communication Interface:
  I2C
What does this measure:
  Ambient Light, 0.005 to 40k lx
  Individual photo diode ADC output for Red, Green, and Blue output
How to Convert:
  Perform 6 Bytes I2C Data Read (2 Bytes for each color: Red, Green, Blue)
  Format 2 Bytes of Data into 16bit values for RED, GREEN, and BLUE intensity values
Typical Use Cases:
  Color Balancing (Lighting)
  Industrial Machinery (Defect Detection)

## Slide 17: Sensor Explanation: KX122 Accelerometer Sensor
Datasheet:
  http://kionixfs.kionix.com/en/datasheet/KX122-1037%20Specifications%20Rev%204.0.pdf
Communication Interface:
  I2C
What does this measure:
  Acceleration, 3 Axis, 16bit, ±8g
  Built-in features like Tap/Double Tap Detection, Activity Detection, Free Fall Detection, etc.
How to Convert:
  Perform 6 Byte I2C Data Read
  Format 6 Bytes of Data into the six 16bit raw sensor output (Accel X/Y/Z)
  Convert Using Appropriate Scheme
    ACCEL = Axis_ValueInG = MEMS_Accel_axis / 16384
Typical Use Cases:
  Built-in Features (Tap Detection, Activity Detection, Free Fall engine, etc.)
  Low Power Wearable Devices (0.9uA standby, 10uA low resolution mode)

## Slide 18: Sensor Explanation: KXG03 Accel + Gyro Sensor
Datasheet:
  http://kionixfs.kionix.com/en/datasheet/ KXG03%20Specifications%20Rev%201.0.pdf
Communication Interface:
  I2C
What does this measure?
  Acceleration, 3 Axis, 16bit, ±16g
  Angular Velocity, 3 Axis, 16bit, ±2048°/sec
How to convert?
  Initialize Gyro: take readings when Gyro is not moving; save this value as Gyro Offset (RAW value OK)
  Perform 12 Byte I2C Data Read
  Format 12 Bytes into the six 16bit raw sensor output (Accel X/Y/Z, Gyro X/Y/Z)
  Convert Using Appropriate Scheme
    ACCEL = Axis_ValueInG = MEMS_Accel_axis / 16384 (±2g)
    GYRO = Axis_ValueinDegPerSec = MEMS_Gyro_axis * 0.007813
Typical Use Cases:
  6 Axis Motion Sensor (Sensor Fusion via Complimentary Filtering or Kalman Filter)
  9 Axis Motion Sensor by adding Magnetometer Sensor
  Motion Controller (Wii Controller), or Motion Feedback (Quadcopter)

## Slide 19: Sensor Explanation: BM1422 Magnetometer Sensor
Datasheet:
  https://github.com/ROHMUSDC/ROHM_Sensor Platform_Multi-Sensor-Shield/blob/master/Documentation/Sensor%20Datasheets /ROHM_MAG-IND_BM1422GMV.pdf
Communication Interface:
  I2C
What does this measure?
  Magnetic Flux, 3 Axis, 16bit, ±1200µT, 0.042µT/LSB
How to Convert:
  Perform 6 Byte I2C Data Read
  Format 6 Bytes of Data into the three 16bit raw sensor output (Mag X/Y/Z)
  Convert Using Appropriate Scheme
    MAG = Axis_ValueInuT = Mag_axis_RawOut * 0.042
Typical Use Cases:
  9 Axis Motion Sensor (by adding Accel+Gyro Sensor)
  E-compass
  Contactless Current Sensor